## Slide 1: Power Aware Computing and Communication Power Management in Past and Present JPL/NASA Missions
Sept. 26, 2000

## Slide 2: Outline
Past Missions - Mars Pathfinder Rover
“Sojourner”
Present Missions - Athena/Mars ‘03 Rovers
MUSES-C Asteroid Nanorover

## Slide 3
Past Missions – Mars Pathfinder
“Sojourner”
The Mars Pathfinder Microrover Flight Experiment
Alpha Proton X-ray Spectrometer (APXS)

## Slide 4
Past Missions – Mars Pathfinder
Mars Rover Power management
  Mission requirement
    Imaging and scientific experiments
  Power supply
    Non-rechargeable battery and solar panel
  Power management solution
    Serialize all operations to avoid exceeding power supply margin

## Slide 5
Past Missions – Mars Pathfinder
Mars Rover Power Management – walking mode
  System specifications
    Six driving motors for wheels
    Four steering motors
    Heaters for each motor
    System health check
    Hazard detection
  Timing constraints and power constraints
  Solutions
    Serialize each operation to satisfy power constraint
    Too conservative usage of power
    No scheduling tool is used

## Slide 6
MFEX Power Requirements
Energy Required
Function
Time and Calculation
7.51W-hr
5.63W-hr
6.92W-hr
1.83W-hr
0.45W-hr
1.2W-hr
5.2W-hr
0.63W-hr
15.0W-hr
50W-hr
95W-hr
motor heating: 1 motor at a time
motor heating: 2 motors at a time
driving (extreme terrain @ -80degC)
hazard detection
imaging (3 images @ 2 min/image)
image compression (compress 3 images @ 6 min/image)
6Mbit communication @ 50min/sol
42, 10 sec health checks during day
remainder of 7 hr daytime CPU operation
WEB heating (as needed)
= 7.51W x 1hr
= 11.26W x 0.5hr
= 13.85W x 0.5hr
= 7.33W x 0.25hr
= 4.5W x 0.1hr
= 3.7W x 0.3hr
= 6.27W x 0.8hr
= 6.27W x 0.1hr
= 3.7W x 4hr
= 50W-hr
Microrover Flight Experiment “Sojourner”

## Slide 7
Microrover Flight Experiment “Sojourner”
Power Subsystem Features - Highlights
The rover power subsystem includes flat GaAs solar panel, a lithium primary (non-rechargeable) battery pack, three DC/DC converters, two switching down regulators, one linear regulator, two inverters, and one current limiter. Switched bypass of the current limiter is provided for battery powered driving and modem heating when solar panel power is inadequate .
Solar array - 14.9 W maximum on Mars noontime power @ ≈ 14 V, could be attenuated by approximately a factor of two during severe dust storms.
The Lithium main battery pack contains ≈ 150 W-hrs of energy, output voltage is ≈ 8 to 11 V (temp/load dependent) . Primary battery energy consumption in the nominal mission is less than 32 W-hr total.
The regulated power-supplies maintain their output voltages over an input range of 8 to 24 V. This permits operation of rover electronics at nominal voltages even though the solar panel output swings from ≈ 14 V to ≈ 18.0 V (due to load/temperature variations), and the rover battery supplies ≈ 8 to 11 V.
The unregulated DC bus supplies power only to converters, regulators, & current limiter.

## Slide 8
Microrover Flight Experiment “Sojourner”
Power Subsystem Features/Implementation
To maximize the available current for driving, many rover actions are sequential, rather than simultaneous, for example:
a) Steering motors are run only when wheel drive motors are stopped, and vice versa.
b) All motors are stopped when laser range-finding/hazard-detection is done (approximately once every wheel radius of travel).
c) RF communication with the lander is not done when motors are running.
d) A bank of motors ( 6 drive-wheel-motor bank, or 4 steering-motor bank) is ripple started, one motor at a time on ≈ 50 msec centers, to assure maximum available startup surge current for each motor.
Solar panel powered WEB (warm electronics box) heating is done whenever the sun is shining and motors/motor-heaters are off.
To minimize energy loss, power for the motors and heaters is routed directly from the core bus through only a “low on-impedance” current limiter (no power converters).

## Slide 9
Microrover Flight Experiment “Sojourner”
Power and Thermal Management – Software Control
Controls the WEB (warm electronics box)heater to maintain the desired WEB temperature and solar panel loading, controls a modem heater, and controls heaters in the motors to reduce gearbox friction.
The basic strategy is to dump all extra solar power (but no battery power) into the WEB heater without overheating the WEB or interfering with command execution.
Current limiting hardware prevents battery drain by heaters, but can be bypassed by setting the corresponding flags.
Heaters are turned off if the core bus voltage is below a threshold (indicating that the current limiter isn't working).

## Slide 10
Microrover Flight Experiment “Sojourner”
Power Switching – Software Control
Turn on or off selected devices, using "shadow" registers in RAM to preserve the state of other devices. In some cases, multiple switches may be associated with a single device (e.g. turning on an upstream power converter), and multiple devices may be associated with a single switch. The power switching functions handle this by turning on all necessary switches to enable the specified devices, and turning off shared switches only when all associated devices have been set to off.
Ensure that relays are never switched while upstream power is enabled, and power converters are turned on with sequencing and delays as needed for the enable/switching controls.
Since the APXS (Alpha Proton X-ray Spectrometer) and modem compete for the same power source, the function to turn the modem on and off checks the current state of APXS control. If the APXS is active, it is sent a "stop collection" command before being powered off to turn on the modem, then powered back on and sent a "resume collection" command when the modem session is finished.

## Slide 11
Microrover Flight Experiment “Sojourner”

## Slide 12: Lessons Learned
Sequential operation rather than simultaneous
No dynamic scheduling, and no autonomy
No CPU-clocking management
Not enough computing power – limited by the laser striping used for hazard detection
Microrover Flight Experiment “Sojourner”

## Slide 13
Pancam/Mini-TES
Mini-Corer
Instrument Arm Cluster :
Raman Spectrometer
Alpha-Proton-X-Ray Spectrometer (APXS)
Mössbauer Spectrometer
Microscopic Imager
Present Missions – Athena/Mars ’03 Rovers Rover Configuration

## Slide 14: Present Missions – Athena/Mars ’03 Rovers Rover Requirements
GaAs solar panel producing 3hrs of ≥ 50W
Li-ion secondary battery (3, 5amp-hr @ 16V batteries)
6-wheel drive, 4-wheel steerable, ‘wide-body’ rocker-bogie chassis
Orbiter relay PSK UHF communications; wire loop antenna on rover
Sample cache for temporary storage of core and soil samples, then (up to 3) transfers of samples.
Electronics and batteries in warm electronics box (WEB)
Hazard range detection system mounted on front and rear below solar panel
Boom mounted stereo cameras for navigation/tracking
Cameras mounted to monitor sampling/sample transfer operations.
Computing system: main electronics in WEB
Charger board manages battery charge/discharge
LMRE (Lander Mounted Rover Equipment) consists of
  pyro releases of rover tiedowns , ramps
  Cable cutters for direct access power/data lines, purge line
  motor actuated ramp deployment
  rail/guide system provides mechanical alignment for docking rover; ‘speed bumps’ and contact sensors define position for sample transfer
  electronics for motor drive, radio

## Slide 15: Athena/Mars ‘03 Rovers - Power Subsystem Requirements
The Athena Rover Power Subsystem is Capabilities driven
Solar array capable of power output associated with 55 parallel strings of 20 cells each of 2cm x 4cm GaAs/Ge cells.
Secondary battery capable of 10 Amp-hrs at end of mission with 50% redundancy, with less than 3 kg mass and 2 liter volume.
Charge control to allow safe charge of secondary batteries.
Provide conditioned power to meet internal loads.
Provide the mission clock and load monitoring when CPU off.
Operational temperatures within WEB is +/- 40oC
  Qualification temperature range is +/- 55oC
Temperature range outside of WEB is +40oC to -90oC
  Qualification temperature range is +55oC to -105oC

## Slide 16
1.2sq m solar panel populated with 55 diode isolated strings of 20, 2cm x 4cm GaAr/Ge cells each string.
Li-ion secondary batteries configured in 3 strings of 5amp-hr @ 11-16V each
Mission clock / alarm clock runs on secondary batteries backed up by primary lithium thionyl-chloride batteries
Battery charger board operates continuously at low power (200mW) performing battery temperature monitoring, cell charging, switching and panel power shunting.
  Shunt radiator is mounted on rocker/bogies structure
Regulated power for cameras.
Athena/Mars ‘03 Rovers - Power Subsystem Specifications

## Slide 17
Power utilization:
  38 W = 19 W (CPU&I/O) + 9 W (accel and gyro) + 10 W (wheel motors) for driving.
  75 W = 19 W (CPU&I/O) + 55 W (transmission) for orbiter communication
  30 W = 19 W (CPU&I/O) + 10 W (transmission) for lander relay communication
  55 W = 19 W (CPU&I/O) + 33 W (peak motor) for drilling
  29 W = 23 W (CPU&I/O) + 6 W (cameras) required for imaging
  11 W Raman, 1.4W APXS and 2.3 W for nighttime spectrometer operation
  141Whr daily for housekeeping engineering
  75Whr limit for nighttime operations
Athena/Mars ‘03 Rovers - Power Subsystem

## Slide 18: Present Missions – MUSES-CN Asteroid NanoRover
The nanorover is designed to be completely solar powered, requiring only 1 watt, including an RF telecommunications system for communications between the rover and a lander or small-body orbiter for relay to Earth.
The power source is 500 grams of commercial, non-rechargeable, replaceable lithium batteries, with energy density of 750 joules per gram.

## Slide 19: Present Missions – MUSES-CN Asteroid Rover
Nanorover command - specific power monitoring and
CPU speed control
  Assumptions/justification –
    Power drawn by CPU is significant and dependent on clock speed
    Some functions require higher clock speed compared to nominal operations, such as:
      communications - keeping up with modem, computing EDAC, protocol response times
      imaging - keeping up with image sensor, compute-intensive algorithms like compression
      response time to sensor events
      hopping – rapid response on motor and attitude control
  While idle (in between commands), rover CPU runs at a parameter-specified idle speed
  For each command, an estimated device power is calculated (not counting CPU), as well as estimated CPU speed required. Power requirement corresponding to a given CPU speed are calculated and tabulated.

## Slide 20: Present Missions – MUSES-CN Asteroid Rover
To run a command: (Example)
  Determine available solar power.
  Minimum required power = device power + CPU power
  If available power is less than minimum required:
      if parameter enables re-orienting , re-orient to maximize solar power
      if still not enough and parameter enables waiting, wait up to parameter limit for solar power
      if still not enough, abort command
  Set CPU speed to maximum allowable based on (power available) - (minimum needed for devices)
  Perform command: during command execution, if power drops significantly (or load shed indication?...):
      CPU speed is reduced to minimum required
      Operate motors one-at-a-time
  Return CPU speed to parameter-specified idle